## Slide 1
Quantitative helium-beam radiography (αRad) with high-energy beams
T. Gehrke1,2,3
M. Metzner2,3, Yanting Xu2,3, F. Kehrein2,3, R. Hermann1,4,5, C. Schömers4, S. Scheloske4, S. Brons4, A. Peters4, O. Jäkel2,3,4, M. Martisikova2,3
1 Department of Radiation Oncology, Heidelberg University Hospital, Im Neuenheimer Feld 400, Heidelberg, Germany
2 Department of Medical Physics in Radiation Oncology, German Cancer Research Center (DKFZ), Im Neuenheimer Feld 280, Heidelberg, Germany
3 Heidelberg Institute for Radiation Oncology (HIRO), National Center for Radiation Research in Oncology (NCRO), Im Neuenheimer Feld 280, Heidelberg, Germany
4 Heidelberg Ion-Beam Therapy Centre (HIT), Im Neuenheimer Feld 450, Heidelberg, Germany
5 Goethe University Frankfurt, Institute of Applied Physics, Frankfurt, Germany

## Slide 2: Helium-beam radiography (αRad) – Application in Ion-beam therapy
Important to detect any uncertainty on the treatment day
  like anatomical changes or
  uncertainties on relative stopping power (RSP)
  based on x-ray CT
Low-dose αRad @ day of treatment
4He
@ high energy
WETmeas = WETCT
?
4He
@ high energy
WETmeas = WETCT
?
Verification of WET-map
from planning CT in treatment position!
Direct information on :
avoiding conversion
from photon-imaging
to physics of ions.
Proton radiography for QA:
Schneider et al., 2004; MedPhys 22(4) &
Low-dose ion imaging:
Collins-Fekete et al., 2021; PMB 66(105009)
Simultaneous patient-positioning is feasible

## Slide 3: Ion imaging – Detection systems worldwide
Bergen pCT group:
  2017 – 2021
  building single-sided detection systems
  Incredible amount of 4644 MAPS chips
4He
@ high energy
WETmeas = WETCT
?
US pCT group:
  2002 – 2016
  built phase I & II detection systems
  considered to be gold standard system
Front & rear trackers (silicon strip detectors)
E/Range detector (scintillator & PMTs)
CAD model (Alme et al 2020, Front. Phys.)
Even more groups: OPTima @ The Christie (UK); ProtonVDA company @ Chicago Proton Center (US)

## Slide 4: Ion imaging – Our current detection system
4He
@ high energy
WETmeas = WETCT
?
αRad at HIT/DKFZ/UKHD
  2016 – now
  Compact and very thin
US pCT group:
Front & rear trackers (silicon strip detectors)
E/Range detector (scintillator & PMTs)

## Slide 5: Detection system – based on silicon pixel detectors
sensitive
Si-layer+
TPX chip
read-out interface
Position + time
MLP:Schulte et al., 2008, Med.Phys. 35(11)
Collins-Fekete et al., 2015, PMB 60(13)
Position + dE + ion ID
operating
principle
MLP:Schulte et al., 2008, Med.Phys. 35(11)
Collins-Fekete et al., 2015, PMB 60(13)
Timepix: Llopart et al., 2007, NIM A 581(1-2)
Detection system: Gehrke et al., 2018, PMB 63 035037; Amato et al., 2020, MedPhys 47(5)

## Slide 6: Previous results & current research questions
…for head-sized objects:
  Spatial resolution (SR) MTF10%=0.6 lp/mm
  WET resolution 0.6 % @ 350 µGy, 0.22 mm pixel pitch
  (object’s WET =190 mm)
Can we perform quantitative αRad, i.e. obtain WET maps?
Can we image the pelvis/abdomen region (WETs up to 320 mm) with sufficient image quality?
Spatial & WET resolution: Gehrke et al., 2018, PMB 63 035037;
Amato et al., 2020, MedPhys 47(5)

## Slide 7: Quantitative αRads @ high initial energies → WET maps
Calibration function:
Quality assessment of WET maps
0.7% ≤ σWET ≤ 1.6% for WET range [250 mm, 313 mm]
preliminary
Comparison to US pCT prototype II: 0.8% ≤ σWET ≤ 1.6%, WET range [180 mm, 240 mm]
I Single-ion WET precision (σWET)
Newly established 4He beams at HIT: up to 330 MeV/u → 600 mm range
dE/dx – WET:
Bortfeld, 1997, MedPhys 24(12)
WET precision, US pCT phase II:
Bashkirov et al., 2016, MedPhys 43(2)

## Slide 8: Quality assessment of WET maps
II Spatial resolution (SR)
  MTF10%= 0.46 lp/mm @ WETobj = 286 mm!
Comparison to HeRad with US pCT prototype II: MTF10%= 0.61 lp/mm @ WETobj = 100 mm
III WET accuracy
Ground truth (GT)
αRad
GT ∗ GaussKernel
Rel. difference map
preliminary
HeRad with US pCT II - SR:
Volz et al., 2017, CDBME 3(2)
MAPD=0.22 %

## Slide 9: Conclusion
The presented method provides helium-beam radiographs with high image quality even for thick objects (~300 mm WET):
  Single-ion WET precision: < 1.6 %
  WET accuracy: MAPD=0.22 %
  Spatial resolution: MTF10%=0.46 lp/mm
Visual indication that imaging of thin & head-sized objects works:
1.5 σ, 10 ions per pixel => 0.8 % vs. 2.4 % of CT
vs. 0.33 lp/mm of CT1.5 mm slice thickness
DECT
αRad